Laboratorio di Sistemi Operativi
Anno Accademico 2006-2007
Software Development with uMPS
Part 2
Mauro Morsiani
Copyright © 2007 Mauro Morsiani
Permission is granted to copy, distribute and/or modify this document under the terms of the GNU Free Documentation License, Version 1.2 or any later version published by the Free Software Foundation; with no Invariant Sections, no Front-Cover Texts, and no Back-Cover Texts. A copy of the license can be found at: http://www.gnu.org/licenses/fdl.html#TOC1

---
uMPS software development
Software development with uMPS architecture:
  - Assembly language development is cumbersome: only ROM and specific HW interface libraries require to be developed in Assembly
  - C language (and GNU gcc compiler) is the preferred alternative
  - The use of a compiler requires a number of conventions to be defined:
    - memory layout and program structure
    - register usage conventions
    - object and executable file formats

---
A generic program memory layout:

---
Generic program memory layout explained:
  - one program in memory = four areas:
    - .text area: contains the code instructions, is typically read-only
    - .data area: contains the program static data (variables, arrays, etc.); it may be subdivided into:
      - .data proper: for data already initialized when program starts
      - .bss (block started by symbol): for other variables and static data
    - heap: contains the program dynamic data (malloc’d structures allocated at runtime: it requires an OS to manage them)
    - stack: for procedure calls management
  - All these areas will have specific addresses in memory
  - The executable file may contain only .text and .data areas

---
uMPS program memory layout:
  - Actually, two types of programs may exist in uMPS:
    - kernel and kernel-like programs, starting with VM off
    - user programs running with VM on
  - uMPS memory layout for kernel programs:
    - .text area: starts at 0x2000.1000 (first frame in RAM is reserved to ROM handlers) and is padded to a multiple of 4KB
    - .data area: starts from the next 4KB frame right after .text area
    - heap: not available (no OS to manage it, remember?)
    - stack: starts from RAMTOP and grows down

---
uMPS program memory layout (cont’d):
  - uMPS memory layout for programs running with VM on:
    - .text area: starts at 0x8000.0000 (first address in virtual memory kuseg2 segment) and is padded to a multiple of 4KB
    - .data area: starts from the next 4KB frame right after .text area
    - heap: available if the OS supports it
    - stack: starts from 0xBFFF.FFFC (OS may decide to use another value) and grows down
  - The memory layout is provided to the compiler using elf32*.x configuration files
  - different files exist for big- and little-endian uMPS, and for kernel and user programs

---
uMPS register usage conventions:

---
uMPS register usage conventions (cont’d):
  - Some interesting registers:
    - $v0: contains the return value when C functions return
    - $a0-$a3: contain the first four parameters in a C function call
    - $sp: stack pointer
    - $fp: frame pointer (in the stack)
    - $gp: global pointer to the GOT (Global Offset Table), a special data structure built by the compiler in the .data area for holding addresses and offsets to access global data structures, function tables and so on
    - $k0-$k1: reserved to ROM handlers usage

---
uMPS stack frame layout:

---
Compilation is a complex process:
  - Four compilation stages:
    - pre-process
    - compile
    - assemble
    - link
  - Usually governed by Makefile and make
  - GNU gcc compiler final output: an ELF (Executable and Linking Format) executable file
  - ELF requires a OS to be loaded: too complex for uMPS kernel or bootstrap ROM
  - a different file format is required

---
Who converts ELF to uMPS file format(s)?
  - umps-elf2umps takes an ELF binary (executable or object file) in input and produces:
    - *.rom.umps: ROM files
    - *.aout.umps: user programs using VM
    - *.core.umps: the format used for kernel files
    - *.stab.umps: a symbol table (a text file describing the symbols’ names and addresses in the executable) associated to the matching .aout.umps or .core.umps file

---
The uMPS .aout format:

---
uMPS .aout header explained:

---
uMPS file formats compared:
  - .rom file format is just bare code: no file headers, .text, .data…
  - .aout and .core file formats are the same
  - .aout program layout will use virtual memory addresses (0x8000.0000 and so on)
  - .core program layout will use physical memory addresses (0x2000.1000 and so on)
  - .core .data area is provided with a zero-filled .bss

---
C language development in uMPS:
  - To develop software in C language for the uMPS architecture, some C conventions must be satisfied:
    - Register usage (as shown)
    - Memory layout (as shown)
    - Who calls main()?
    - The linker expects a __start() function to exist
    - It is provided in:
      - crtso.o for kernel and programs running with VM off
      - crti.o for user programs running with VM on
  - But who calls __start()?

---
The ROM strikes once again:
  - The Bootstrap ROM is able to access the .core file in memory (or to load it from tape) and to start the kernel
  - The ROMs are also responsible for exception and TLB-refill handling
  - Is there something else the ROMs can perform to help us?
  - Yes: handling the start of new processes and the kernel program termination

---
ROM support routines:
  - accessible only in Kernel mode
  - using physical addresses
  - invoked by raising a BREAK exception

---
libumps: uMPS support library
  - libumps acts as a wrapper, allowing to:
    - access ROM routines
    - access special CP0 registers
    - issue TLB-related and SYSCALL instructions
  - libumps is composed by two parts:
    - libumps.e: to be included in C programs source (see it for library description and details)
    - libumps.o: to be linked with other object files to make an executable file

---
libumps library kernel support functions:
  - unsigned int SYSCALL(unsigned int number, unsigned int arg1, unsigned int arg2, unsigned int arg3): generates a SYSCALL exception
  - unsigned int STST(state_t * statep): saves the current status of the processor

---
libumps library functions for CP0 register access:

---
libumps library functions for CP0 register access (cont’d):

---
libumps library functions for TLB-related instructions: