Laboratorio di Sistemi Operativi
Anno Accademico 2006-2007
uMPS Introduction
 Part 3
Mauro Morsiani
Copyright © 2007 Mauro Morsiani
Permission is granted to copy, distribute and/or modify this document under the terms of the GNU Free Documentation License, Version 1.2 or any later version published by the Free Software Foundation; with no Invariant Sections, no Front-Cover Texts, and no Back-Cover Texts. A copy of the license can be found at: http://www.gnu.org/licenses/fdl.html#TOC1

---
uMPS processor architecture
The uMPS architecture

---
uMPS devices and I/O management
uMPS devices and interfaces:
  - uMPS provides a basic set of devices:
    - TOD clock and interval timer
    - disks
    - tapes
    - ethernet-like network interfaces
    - printers
    - tty-like terminals
  - each device class is associated to a specific interrupt line
  - for each device class (not TOD) up to 8 devices may be installed
  - each device is operated by a controller
  - the processor talks with controllers using device registers
  - device registers are locations in memory
  - all addresses in I/O management are physical memory addresses

---
Device register structure:
  - Each device register has a base address
  - All device registers (except TOD) have the same basic structure
  - Device register commands and status codes for each device class are (obviously) different, but share a common operation logic

---
Device registers structure (cont’d):
  - only some device registers are writable
  - device registers are writable only when device is idle
  - device registers “freeze” when an operation is in progress
uMPS processor-device communication protocol:
  - is a full-handshake interrupt-driven protocol
  - full-handshake: each exchange has to be acknowledged explicitly
  - interrupt-driven: interrupts are used to notify the CPU that something has happened

---
uMPS processor-device communication protocol details:
  - the CPU initiates an operation by writing a command in a device register
  - the device starts the operation and sets some “working…” status code in the device register
  - the device completes the operation and:
    - sets some “completed…” status code in the device register
    - raises an interrupt by asserting (setting on) an interrupt line
  - the CPU:
    - may check the operation outcome (by looking at the status code in the device register)
    - may acknowledge it (by issuing an acknowledge command): this deasserts (turns off) the interrupt line
  - An optimization: a new command implicitly acknowledges a previous operation

---
Interrupt line vs. device class:
  - higher line # : lower speed/priority

---
How to handle a lot of devices:
  - TOD/Interval Timer + (5 lines x 8 devices) = 41 possible devices
  - only 6 interrupt lines
  - How to know which devices are installed?
  - How to understand which devices have raised an interrupt?
  - Where to put all these device registers?

---
How to handle a lot of devices (cont’d):
  - How to know which devices are installed?
    - with an Installed Devices Bit Map (a 1 in the map means the device is present)
  - How to understand which devices have raised an interrupt?
    - with an Interrupting Devices Bit Map (a 1 in the map means the device is raising an interrupt)
    - This also means: an interrupt line will remain asserted until all device interrupts pending on that line get acknowledged

---
uMPS memory management
Where to put all these device registers?

---
Device Register Area details:

---
Device Register Area details (cont’d):
  - Bus Register Area: TOD/Interval Timer and and other useful information (RAMSIZE, etc.)

---
Device Register Area details (cont’d):
  - Special device registers in the Bus Register Area:
    - TOD (TODHI + TODLO) (64 bit, readonly): number of clock ticks from last boot/reset
    - Interval Timer (read/write):
      - starts from 0xFFFF.FFFF at boot/reset
      - gets decremented by 1 on each clock tick
      - raises an interrupt on line 2 when an underflow happens (0x0000.0000 → 0xFFFF.FFFF transition)
    - Time Scale (readonly): number of clock ticks per microsecond

---
Installed Devices Bit Map and format:
  - Devices are numbered 0..7

---
Interrupting Devices Bit Map and format:
  - Devices are numbered 0..7

---
Where is my device?
  - Given a device identified by:
    - an interrupt line (IntLineNo)
    - a device number (DevNo)
  - The base address of the corresponding device register is:
  - devAddrBase = 0x1000.0050 + ((IntlineNo - 3) * 0x80) + (DevNo * 0x10)

---
Device register structure:

---
Disk device:
  - DMA (Direct Memory Access) capable
  - 4 KB block size
  - up to 64K cylinders, 256 heads, 256 sectors
  - disk geometry: Cylinder/Head/Sector (CHS)
  - geometry packed in DATA1 field
  - numbered starting from 0, up to MAX{CYL/HEAD/SECT} -1

---
Disk device commands:

---
Disk device COMMAND field format:

---
Disk device STATUS codes:

---
Tape device:
  - DMA capable
  - read-only
  - employed to load programs and data files
  - 4 KB block size
  - DATA1: tape marker under head
  - no tape: DATA1 = end-of-tape (EOT)

---
Tape device DATA1 codes:
  - Tape = TS EOB EOB .. EOF EOB EOB ..EOF EOB EOB.. EOT
  - EOF stands also for EOB
  - EOT stands also for EOF

---
Tape device commands:

---
Tape device STATUS codes:

---
Network device:
  - DMA capable
  - 1514-byte Ethernet frame size and buffer format
  - 6-byte MAC (Media Access Control) address
  - DATA0 used for buffer address
  - DATA1 reports or sets packet length
  - non-blocking reads (DATA1 == 0)
  - several operation modes

---
Network device operation modes:
  - normal / promiscuous (0x4) mode:
    - normal: only broadcast and packets explicitly directed to the interface are listened to, others are ignored
    - promiscuous: all packets are listened to
  - polling / interrupt driven (0x2) mode:
    - polling: packet reads must be explicit (no interrupts)
    - interrupt driven: receiving a packet raises an interrupt
  - named (0x1) / unnamed mode:
    - named: transmitted frames are tagged with the MAC address of the device
    - unnamed: the device does not modify the MAC address provided for transmitted frames

---
Network device commands:

---
Network device DATA0 and DATA1 layout in CONFIGURE and READCONF:

---
Network device STATUS codes:

---
Printer device:
  - simple parallel line printer
  - character-based
  - DATA0: character to be printed
  - DATA1: unused

---
Printer device commands:

---
Printer device STATUS codes:

---
Terminal device:
  - serial line terminal for basic I/O interactions
  - 8-bit character
  - two sub-devices: transmitter and receiver
  - both sub-devices will raise interrupts

---
Terminal device commands:

---
Terminal sub-device COMMAND format:

---
Terminal sub-device STATUS codes:

---
Terminal sub-device STATUS format:

---
Things to remember:
  - First write parameters (DATA0, DATA1) then COMMAND
  - Check STATUS after operations
  - Remember always to ACK commands
  - Beware of DMA